## Slide 1: Rationale for the FLAME Study
Limited high quality data in high-risk PE
Traditional RCT in high-risk PE would be difficult to enroll
  Low incidence (5% of all PE)
  Emergent presentation
  High rate of crossover or combined treatments
FLAME was designed to evaluate outcomes in high-risk PE patients treated with large-bore mechanical thrombectomy or other contemporary treatments
  Designed as a non-randomized study, with a pre-specified performance goal derived from a robust meta-analysis1, as suggested by an AHA Scientific Statement to generate evidence in high-risk PE2
1Silver et al. JSCAI. 2023;2
2Giri et al. Circulation. 2019;140

## Slide 2: FLAME: Trial Design
Prospective, multicenter, non-randomized, parallel group, observational study of high-risk PE
FlowTriever Arm
FlowTriever mechanical thrombectomy as primary treatment
Context Arm
Other non-FlowTriever therapies as primary treatment
Trial Details
*Not shown due to low enrollment (n=1)
Specific treatment not dictated (physician discretion)
Concurrent, non-randomized enrollment
Patients followed through discharge or 45 days
Designed to capture all high-risk PE patients:
  Waiver of consent for unbiased enrollment
  Chart review to ensure no high-risk patients were missed
Prior Therapy Arm*
Lower-risk PE treated with advanced therapy but progressed to high-risk PE
High-risk PE
Patients

## Slide 3: FLAME: Eligibility Criteria
≥18 years of age
Presenting with high-risk PE
PE determined to be cause of shock
One or more of the following:
  Systolic BP <90 mmHg or drop of >40 mmHg for at least 15 minutes
  Need for vasopressor support
  Resuscitation after cardiac arrest with <30 minutes of CPR and Glasgow Coma Scale >8
Inclusion Criteria
Out of hospital cardiac arrest with Glasgow Coma Scale ≤8
Cardiac arrest with ongoing CPR >30 minutes
Contraindication to anticoagulants, i.e. heparin or alternative
Hematocrit <28%
Platelets <25,000/µL
INR >8
Intracardiac thrombus or clot in transit
Anaphylactic sensitivity to radiographic agents
History of pulmonary hypertension with systolic PA pressure >70 mmHg
Chronic medical conditions with <90 days of life expectancy
COVID-19 positive
Exclusion Criteria

## Slide 4: FLAME: Endpoints
In-hospital composite:
All-cause mortality
Bailout to alternate thrombus removal strategy
Clinical deterioration
Major bleeding
Primary Endpoint*
*CEC-adjudicated for FlowTriever and Context Arms (BCRI) †Derived from a meta-analysis of high-risk PE outcomes; Silver et al. JSCAI. 2023;2
  FLAME was stopped early after meeting the pre-specified interim analysis criterion at 50 FlowTriever patients
Primary Endpoint Analysis
The FlowTriever Arm primary endpoint was compared to a performance goal of 32% which was established from our published meta-analysis†
A pre-specified interim analysis was planned at 50 FlowTriever patients enrolled
Safety*:
Primary endpoint components, stroke, device-related complications, and access site injury
Utility measures:
Hospital and ICU stay, ECMO use, time to extubation, and discharge location
Secondary Endpoints

## Slide 5: Baseline Characteristics and History
 | FlowTriever Arm (n = 53)
Age, years | 64.8 ± 15.3
Female | 26/53 (49.1%)
BMI, kg/m2 | 32.2 ± 6.1
History | 
Systemic HTN | 37/51 (72.5%)
Pulmonary HTN | 4/48 (8.3%)
PE | 7/53 (13.2%)
DVT | 16/52 (30.8%)
Cancer | 12/53 (22.6%)
Active Cancer | 7/52 (13.5%)
Contraindication to thrombolytics | 22/53 (41.5%)
Absolute | 6/53 (11.3%)
Relative | 16/53 (30.2%)
115 patients from 11 US sites*
*Prior Therapy Arm not shown due to low enrollment (n=1)
Context Arm (n = 61)
61.6 ± 13.9
35/61 (57.4%)
33.9 ± 8.5
41/61 (67.2%)
2/59 (3.4%)
7/60 (11.7%)
12/60 (20.0%)
13/59 (22.0%)
5/59 (8.5%)
7/60 (11.7%)
3/60 (5.0%)
4/60 (6.7%)

## Slide 6: Clinical Presentation
 | FlowTriever Arm (n = 53)
Reason for high-risk PE: Systolic BP <90 mmHg or decrease of >40 mmHg for 15 minutes Need for vasopressor support Resuscitation after cardiac arrest with <30 minutes of CPR and Glasgow Coma Scale >8 | 34 (64.2%) 32 (60.4%) 11 (20.8%)
SCAI shock stage A B C D E | 2 (3.8%) 11 (20.8%) 29 (54.7%) 5 (9.4%) 6 (11.3%)
PE Location Central Lobar Segmental | 49 (92.5%) 36 (67.9%) 27 (50.9%)
Context Arm (n = 61)
31 (50.8%) 46 (75.4%) 20 (32.8%)
1 (1.6%) 6 (9.8%) 22 (36.1%) 12 (19.7%) 20 (32.8%)
40/53 (75.5%) 36/53 (67.9%) 25/53 (47.2%)

## Slide 7: Primary Treatment Details
FlowTriever Arm (n = 53) | FlowTriever Arm (n = 53)
Primary Treatment: FlowTriever | 53 (100%)
Estimated blood loss, mL | 100 [20-240], n = 46
With FlowSaver, mL | 50 [0-200], n = 10
Context Arm (n = 61) | FlowTriever Arm (n = 53)
Primary Treatment: Systemic thrombolytics Anticoagulation alone Catheter-directed thrombolytics Surgical thrombectomy Mechanical thrombectomy | 42 (68.9%) 14 (23.0%) 4 (6.6%) 1 (1.6%) 0 (0%)

## Slide 8: Primary Endpoint
Composite Primary Endpoint: 17.0%*
Composite Primary Endpoint: 63.9%
FlowTriever Arm
Context Arm
*Significantly lower than the performance goal of 32.0% (P<0.01)

## Slide 9: Primary Endpoint Components
Chart: 
| Category 1
Series 1 | 0.019
Series 2 | 0.285
Series 3 | 0.295
In-hospital mortality
FlowTriever Arm
n = 53
Context Arm
n = 61
Performance Goal
Literature-based

## Slide 10: Primary Endpoint Components
Chart: 
| Category 1
Series 1 | 0.038
Series 2 | 0.303
Series 3 | 0.262
Chart: 
| Category 1
Series 1 | 0.151
Series 2 | 0.156
Series 3 | 0.213
Chart: 
| Category 1
Series 1 | 0.113
Series 2 | 0.115
Series 3 | 0.246
Bailout
Clinical deterioration
Major bleeding
FlowTriever Arm
n = 53
Context Arm
n = 61
Performance Goal
Literature-based

## Slide 11: Safety Outcomes
 | FlowTriever Arm (n = 53)
Stroke Ischemic Hemorrhagic | 1 (1.9%) 1 0
Subjects with device-related complication† Most common: Hemoglobin decrease or anemia Vascular access site hemorrhage/hematoma Hypotension | 12 (22.6%) 8 4 1
Context Arm (n = 61)
4 (6.6%) 2 2*
10 (16.4%) 3 4 3
Context Arm:
*ICH in 2/42 (4.8%) patients who received systemic thrombolytics
FlowTriever Arm:
†No reports of device-related tricuspid valve injuries, cardiac injuries, or pulmonary vascular injuries

## Slide 12: Safety Outcomes
 | FlowTriever Arm (n = 53)
Subjects with SAEs | 16 (30.2%)
Subjects with SAEs related to primary treatment device or therapy | 10 (18.9%)
Related to thrombolytic therapy | 0 (0%)
Related to ECMO only | 0 (0%)
Subjects with access site injury requiring intervention | 4 (7.5%)
Context Arm (n = 61)
37 (60.7%)
23 (37.7%)
17 (27.9%)
1 (4.3%)
5 (8.2%)

## Slide 13: Secondary Endpoints
Utility Measures | FlowTriever Arm
Length of stay post-treatment, nights* | 7.0 [3.0-12.5] n = 52
Length of ICU stay post-treatment, nights* | 2.0 [1.0-4.0] n = 52
ECMO use | 3/53 (5.7%)
Time to extubation, days† | 1.6 [1.2-4.3] n = 4
Context Arm
8.0 [6.0-15.0] n = 43
3.0 [1.0-7.0] n = 43
7/61 (11.5%)
1.8 [1.5-3.1] n = 6
Chart: 
| FlowTriever Arm | Context Arm
Expired prior to discharge | 0.019 | 0.295
Other | 0.057 | 0.098
Not discharged | 0.075 | 0
Care facility or skilled nursing home | 0.245 | 0.18
Home with home healthcare | 0.113 | 0.049
Home | 0.491 | 0.377
Discharge Location
FlowTriever Arm
n = 53
Context Arm
n = 61
*In surviving patients †In surviving patients who underwent a single intubation procedure prior to primary treatment and were extubated prior to study exit

## Slide 14: Conclusion
The FLAME study is the largest interventional trial in high-risk PE
Large-bore mechanical thrombectomy with FlowTriever was associated with a significantly lower occurrence of meaningful in-hospital adverse clinical outcomes
  In-hospital mortality, bailout, clinical deterioration, major bleeding
FlowTriever was associated with remarkably low mortality
  FlowTriever Arm: 1.9%
  Performance goal: 28.5%
  Context Arm: 29.5%

## Slide 15: Limitations
Not a randomized controlled trial
Despite efforts, cannot guarantee capture of all high-risk PE patients
Treatment type was at the discretion of treating physician, which may have introduced selection bias
Follow-up limited through discharge, however the highest risk of mortality in high-risk PE is during the index hospitalization

## Slide 16: Implications
Large-bore mechanical thrombectomy with the FlowTriever System likely reduces mortality in high-risk PE patients by rapidly unloading the RV
  Quickly reverses the obstructive shock death spiral
  Simultaneously improves oxygenation
A care pathway similar to STEMI and stroke may benefit high-risk PE patients
  Teams are accustomed to treating critically ill patients with access to hemodynamic assessment and advanced support therapies

## Slide 17: Acknowledgments
Principal Investigators | Sites/Affiliations
Mitch Silver (National co-PI) | OhioHealth Heart and Vascular, Columbus, OH
Jim Horowitz (National co-PI) | NYU Grossman School of Medicine, New York, NY
Sameer Khandhar | Perelman School of Medicine at University of Pennsylvania, Philadelphia, PA
Jay Giri | Perelman School of Medicine at University of Pennsylvania, Philadelphia, PA
Wissam Jaber | Emory University Hospital, Atlanta, GA
Herman Kado | Ascension Providence Hospital, Southfield, MI
Catalin Toma | University of Pittsburgh Medical Center, Pittsburgh, PA
David Zlotnick | University at Buffalo, Gates Vascular Institute, Buffalo, NY
Terry Bowers | Corewell Health William Beaumont University Hospital, Royal Oak, MI
Paul Butros | Inova Health Systems Heart and Vascular Institute, Fairfax, VA
Aaron DuCoffe | Inova Health Systems Heart and Vascular Institute, Fairfax, VA
Lee Greenspon | Lankenau Medical Center, Wynnewood, PA
Bushra Mina | Lenox Hill Hospital, Northwell Health, New York, NY
Mithun Chakravarthy | AHN Cardiovascular Institute at Allegheny General Hospital, Pittsburgh, PA

## Slide 18: Take Home Points From the FLAME Trial
A modern day peer reviewed meta analysis of high-risk PE literature provided the performance goal as a point of reference.
All end points were adjudicated by an independent CEC.
All patients met the modern day definition of high-risk or massive PE.
The context arm provided context and helped capture all high-risk PE patients in the study to assess outcomes.
There was no randomization.

## Slide 19: Take Home Points From the FLAME Trial
The FlowTriever group had a mortality of 1.9% and 17 % of patients reached the composite primary endpoint.
The context arm had a mortality of 29.5 % and 63.9 % reached the composite primary endpoint.
All patients with SCAI shock D/E treated with FlowTriever survived.
46 % of patients with SCAI shock D/E in the context arm died.

## Slide 20: Waiver of Informed Consent >> Confusion
The FLAME protocol was approved by all institutional IRBs.
ALL PATIENTS consented for any procedure by hospital protocol.
The waiver of informed consent was to participate in the registry only.
FDA guidelines were followed for waiver of informed consent:
  No IC needed for an observational registry
  Data all de-identified
  Physician treatment/management was not prescribed or dictated
The AHA scientific statement published in 2019 was followed exactly as recommended…..

## Slide 21: Perspective…
“Treatment type was at the discretion of the treating physician”:
  Experienced PE centers and physicians were chosen by design.
  Was the patient stable enough to reach the cath lab ?
  Was an experienced operator available or even consulted ?
    More patients with advanced shock presented on nights/weekends.
  Was the clot anatomy suitable for FT ?
  Our conclusion is NOT that FT treated patients did better than context arm patients (not randomized by design).
  But that massive PE patients that can be taken to the cath lab treated with FT have very good results.

## Slide 22: THANK YOU